## Slide 1: Carbon disulfide
Robert Hendrickson, MD

## Slide 2: Carbon disulfide
CS2
Production – worldwide
  2 CH4 + S8 → 2 CS2 + 4 H2S
    Natural gas
    Silica gel/alumina catalysts
Notes: Technical grade – sweet smell

## Slide 3: Carbon disulfide
Carbon disulfide –
  Colorless / yellow
  Volatile
    Vapor accumulates along the ground

## Slide 4: Carbon disulfide
Uses:
  Viscose rayon production
  Cellulose production
  Building block for
    Fungicides/soil fumigants
    Xanthates (used in mining)
    Accelerators (for rubber vulcanization)
    Pharmaceuticals
    Carbon tetrachloride
  Solvent

## Slide 5: Viscous Rayon
“Artificial silk”
“Art silk”
Woven & knitted
Easily dyed

## Slide 6: Viscous Rayon
Cellulosic fiber
  Similar to cotton (but polymer length is shorter)
Produced using cellulose:
  Wood pulp
  Bamboo
  Sugar cane
Add sodium hydroxide (alkali cellulose)
Add carbon disulfide (sodium cellulose xanthate)
    Xanthate = ROCS2- Na+

## Slide 7: Viscous Rayon
Sodium cellulose xanthate
  Ripening (polymerization)
Extrude through sulfuric acid
  Yields rayon
    Pure cellulose

## Slide 8: Viscous Rayon

## Slide 9: Viscous Rayon
Extruded through spinnerets
Notes: Each thread = 0.1mm

## Slide 10: Viscous Rayon

## Slide 11: Viscous Rayon

## Slide 12: Carbon disulfide
Exposure:
  Inhalational
  Dermal
Environmental – small amounts
  Volcanic eruptions
  Marshes

## Slide 13: Carbon disulfide
Toxicity – acute exposure (accident)
  Pulmonary/mucosal irritant
  CNS depression
    Kamat SR. Chem Engin World 1994; 29: 107-111

## Slide 14: Carbon disulfide
Toxicity – chronic exposure
  Accelerated atherogenesis, CAD, angina, MI
  233 exposed VR worker & 174 non-exposed
  Control=561 deaths of local men w/o exposure
  Also looked at CV death rate of workers by their jobs within the factory who had > 10 years
Notes: 233 workers worked in the process where CS2 was used. 174 worked at the company, but not in processing and were not exposed.

## Slide 15
% of deaths from CVD:
  42% rayon process workers
  24% other rayon workers
  17% local males

## Slide 16: Carbon disulfide
Notes: 233 workers worked in the process where CS2 was used. 174 worked at the company, but not in processing and were not exposed.

## Slide 17: Carbon disulfide
Toxicity – chronic exposure
  Accelerated atherogenesis, CAD, angina, MI
    Balcarova O, Halik J. 1991. Sci Total Environ 101(l-2): 97-99.
    Hernberg S, Nordman CH, Partanen T, et al. 1971. Work Environ Health 8:11-16.
    Hernberg S, Nurminen M, Tolonen M. 1973. Work Environ Health 10:93-99.
    Nurminen N, Mutanen P, Tolonen H, et al. 1982. Am J Epidemiol 115: 107-l18.
    Sugimoto K, Goto S, Kanda S, et al. 1978. Stand J Work Environ Health 4:151-158.
    Tiller JR, Schilling RS, Morris JM. 1968. Br Med J 4:407-411.
    Tolonen M, Nurminen M, Hernberg S. 1979. Stand J Work Environ Health 5:109-114.
  Increased total & LDL cholesterol
  Decreased fibrolytic activity

## Slide 18: Carbon disulfide
Toxicity – chronic exposure
  Retinal toxicity
    Retinal microaneurysm
    20-25% of workers v 4-8% of controls (Japanese & US, but NOT in Finnish workers)
      NIOSH. 1984a. NTIS/PB85-110229.
      Raitta C, Tolonen M. 1975. Arch Klin Exp Ophthalmol 195:149-54.
      Sugimoto K, Goto S, Kanda S, et al. 1978. Stand J Work Environ Health 4:151-158.
      Sugimoto K, Goto S, Taniguchi H, et al. 1977. Int Arch Occup Environ Health 39:97-101.
      Tolonen M, Hernberg S, Nordman CH, et al. 1976. Int Arch Occup Environ Health 37:249-264.
    Delayed choroidal filling (due to rigid retinal arteries)
Notes: Workers were exposed to 15-35 ppm during the 1950s & 5-15ppm after.

## Slide 19: Carbon disulfide
Toxicity – chronic exposure
  Neuropathy
    Dose related reduction in motor nerve conduction in workers exposed to CS2
      Johnson
      Rujen 90,93
      Sikora 90
  Tremor, parkinsonism
  Cerebral atrophy
    Aaserud 88
  Cognitive/neuropsychological – mixed studies
Notes: Workers were exposed to 15-35 ppm during the 1950s & 5-15ppm after.

## Slide 20: Carbon disulfide
Disulfiram reactions:
  CS2 inhibits aldehyde dehydrogenase slightly
  Unlikely – at 80mg/dL ETOH & 10ppm CS2
    Freundt KJ, Lieberwirth K, Netz H, et al. 1976. Int Arch Occup Environ Health 37:35-46.
Notes: Workers were exposed to 15-35 ppm during the 1950s & 5-15ppm after.

## Slide 21: Carbon disulfide

## Slide 22: Global Harmonized System of Classification and Labeling of Chemicals (GHS)
Labeling:
  Identification of product
  Signal word: Danger or Warning
  Hazard and precautionary statements
  Identity of the supplier

## Slide 23: Global Harmonized System of Classification and Labeling of Chemicals (GHS)

## Slide 24: National Fire Protection Association (NFPA)

## Slide 25: Carbon disulfide
Flammable
“Acute toxicity”
Organ toxicity
3: can cause serious or permanent injury
4: vaporize/burn at normal temp
0: Stable
No “special hazard”

## Slide 26: For more information
https://www.atsdr.cdc.gov/toxprofiles/tp.asp?id=474&tid=84

## Slide 27: Questions and discussion…