## Slide 1: Core Elements of Occupational Health: Hazard Identification and Control, Industrial Hygiene, Ergonomics and Occupational Health Nursing

## Slide 2: Instructors
Dede Montgomery, MS, CIH, Certified Industrial Hygienist Oregon Institute of Occupational Health Sciences, OHSU
Mary Salazar, EdD, RN, COHN, Faculty Member University of Washington
Karin Drake, Assistant Department Administrator Occupational Health, Kaiser Permanente

## Slide 3: Course Objectives
Explain and practice hazard identification within a variety of different types of workplaces common in Thailand.
Determine appropriate hazard controls in response to identification of hazards.
Analyze information related to workplace hazards, such as safety data sheets, websites and industry-related resources.
Learn and practice best practice strategies for occupational health nursing.

## Slide 4: Day 1: Key concepts
Hazard Identification, Evaluation and Control
  Priority industries
Medical Directorship
Planning for Workplace Walkthroughs

## Slide 5: Day 1 & 2 Priority Industries
Manufacturing
  petroleum refining
  chemical
  automobile,
  Other (transportation equipment, electronic, glass, apparel)
Mining: Oil and gas extraction
Services (e.g., healthcare)
Transportation, communications, electric, gas and sanitary services
Others (retail, finance, construction)

## Slide 6: Priority 1 - Manufacturing: Top Hazards
Chemicals
Falls
Heavy Machinery (exposure to moving parts, guarding, caught between)
Fire
Confined spaces
Musculoskeletal disorders

## Slide 7: A. Manufacturing Hazards: Automobile
Health
Noise
Musculoskeletal injuries (sprains, strains, overuse)
Chemicals: especially solvents and other volatile vapors; molten metal spills and carbon monoxide; coolants; chromic and sulfuric mist.
Confined space entry
Safety
Uncontrolled release of energy
Heavy machinery
Falls
Forklifts, cranes, heavy equipment
Crushing and cuts

## Slide 8: Automobile manufacturing

## Slide 9: Auto manufacturing tasks: top health hazards
Foundries: Molten metal spills and explosions, carbon monoxide, foreign body, contusion and burn injuries. Some increased lung cancer risks.
Machining: Carcinogen exposures from chemicals (coolants), occupational asthma, respiratory symptoms.
Hardware and electroplating: Cancer risk when chromic and sulfuric mist exposures.
Vehicle assembly: Cumulative trauma disorders.

## Slide 10: B. Manufacturing: Chemicals
Commodity chemicals
  Polymers (polyethylene, PVC, polyester, etc.)
  Petrochemicals (made from liquefied petroleum gas, natural gas, crude oil and include benzene, toluene, methanol, etc.)
  Inorganic chemicals (salt, chlorine, soda, acids, hydrogen peroxide)
  Fertilizers (ammonia, phosphates, potash)
Life sciences
  Pharmaceuticals, vitamins, pesticides, animal health products.
Specialty chemicals
  Industrial gases, electronic chemicals, adhesives, coatings
Consumer products
  Soaps, detergents, cosmetics
Notes: Exposures vary by type of operation and controls available.

## Slide 11: C. Manufacturing: Petroleum refineries
A refinery splits crude oil into its many parts which are then reprocessed into useful products.
Oil refineries are tightly regulated work places.
Products produced include: fuels, petroleum solvents, lubricating oils, petroleum wax, greases and asphalt.
Routine operations present low exposure risks when adequate maintenance is carried out and design construction standards have been followed.
  The potential for exposures always exists, however.

## Slide 12: Petroleum refineries: top hazards
Hazardous chemicals – fire, explosion, toxicity, corrosiveness, asphyxiation.
  Fire and Explosion: principal hazards.
  Health hazards: Hydrocarbon vapors, sulfur dioxide, carbon monoxide, nitrogen dioxide, hydrogen sulfide, particulates, chlorine, ammonia.
  Shutdown and maintenance work times: require careful planning and procedures to make sure that unanticipated exposures don’t occur.
  Confined space work and tank cleaning: concern about hydrogen sulfide exposure. Processes may use hydrofluoric acid and other “washes.”
  Use of permit systems.
  Emergency warning systems and procedures.

## Slide 13: Priority 2 - Oil and Gas Extraction: Top causes of fatalities
Health
Explosions and Fires
Confined Spaces
Chemical Exposures
Safety
Vehicle Accidents
Struck-By/ Caught-In/ Caught-Between
Falls
Notes: Culture: process safety management
Putting productivity ahead of safety
No second checks in systems

## Slide 14: Oil and Gas Extraction: Confined Spaces
Workers are often required to enter confined spaces (storage tanks, mud pits, reserve pits and excavations, sand storage containers, and spaces around a wellhead).
  Safety hazards = ignition of flammable vapors or gases.
  Health hazards = asphyxiation and exposure to hazardous chemicals.
  These spaces must be tested using direct-reading instruments.
Notes: Confined space permit system

## Slide 15: Oil & Gas Extraction: Health Hazards
Hydrogen sulfide
Noise
Diesel Exhaust
Silica exposure during processes that use sand.
Hazardous chemicals used during processes.
Naturally occurring radiation.
Tips to control:
  Identify type, extent and source of hazard.
  Inform and educate: Safety data sheets
  Consider PPE

## Slide 16: H2S Confined Space Entry Incident

## Slide 17: Fatality case study
Warning signs and symptoms: dizziness, confusion, immobility, and collapse
Notes: : In some regions, workers gauge oil tanks by opening tank hatches, visually observing liquid levels, and then manually measuring liquid oil levels.
Between 2010-2015 9 U.S. oil and gas extraction workers died following exposure to hydrocarbon gases and vapors and oxygen deficient atmospheres after opening hatches of carbon storage tanks.
Worker peers down an open hatch of the oil tank.
Fixed oil tanks often are interconnected allowing contents to equalize over multiple tanks. Equalization of tanks can result in a high volume of off-gassed vapors when a tank hatch is opened.
The windsock is a visual indicator for the worker to stay positioned upwind while gauging.

## Slide 18: Tools: Hydrogen Sulfide Gas
https://www.osha.gov/SLTC/etools/oilandgas/general_safety/h2s_monitoring.html

## Slide 19: Napo Films: Danger Chemicals!

## Slide 20: Priority 3: Services (including health care)
Hazards vary depending on work environment.
  General safety (slips, trips and falls; electrical; machinery; driving)
  Chemicals when used.
  Biological (needles and other exposures in healthcare)
  Ergonomic (repetitive motion, lifting, sitting)
  Other health (noise, stress, radiation)

## Slide 21: Priority 4: Transportation, Communications, Energy
Hazards vary depending on work environment, and include many we have discussed already.
Hazards particular to Electric Power Industry:
  Electrocution
  Falls
  Confined Spaces
  Fires and Explosions
  Sprains, Strains, and Fractures
  Thermal Stress