## Slide 1: Outdoor air pollution
Robert G. Hendrickson, MD
Oregon Poison Center
Oregon Health and Science University
Portland, Oregon, USA

## Slide 2: Consider this day…
You are working in an emergency department (ED)
On the way to work, your eyes are watering a bit and you develop a mild cough
In the ED:
  100% increase in patients today
  4X the number of intubations today
  ICUs are full
  Only a few ventilators left in the hospital

## Slide 3: Consider this day…
What is going on?
  Industrial release?
    Chlorine, ammonia, ?
  Terrorist attack?
    Nerve agent?
    Vesicants?
  No pattern to the patients, no common exposure except that they all live in the local city…

## Slide 4
Notes: Shanghai

## Slide 5: Outdoor air pollution
What is outdoor air pollution?
  Gases & fine particles produced from natural and man-made activities
  Smog = used to describe mixture of smoke/pollution and fog

## Slide 6: Bangkok

## Slide 7: Los Angeles, USA

## Slide 8: Outdoor air pollution
What is outdoor air pollution?
  Oxides of nitrogen (e.g. nitrogen dioxide, NO2)
  Sulfur dioxide (SO2)
  Ozone (O3)
  Carbon monoxide (CO)
  Particulate matter (PMs)
  Lead, metals, and other hazardous air pollutants (HAPs) or “air toxics”

## Slide 9: Outdoor air pollution
London, Dec 5-9, 1952
  Great Smog of ’52
  Sulfur dioxide
  4-12,000 deaths
  100,000 made ill
"Nelson's Column during the Great Smog of 1952" by N T Stobbs. Licensed under CC BY-SA 2.0 via Commons - https://commons.wikimedia.org/wiki/File:Nelson%27s_Column_during_the_Great_Smog_of_1952.jpg#/media/File:Nelson%27s_Column_during_the_Great_Smog_of_1952.jpg
Notes: Cold weather = more coal burning
Anticyclone = windless London and temperature inversion
Visibility decreased to 1 meter – difficult to walk outside
Smog penetrated indoors and theaters closed

## Slide 10: Outdoor air pollution
Eastern China, 2013
  Shanghai
  Tianjin
AQI = 507
Airports, highways closed due to poor visibility
"Shanghai haze in Huangpu Distract 20131206" by Galaxyharrylion - Own work. Licensed under CC BY-SA 3.0 via Commons -
by Jeff Schmaltz - NASA Earth Observatory. Licensed under Public Domain via Commons -
Notes: AQI >300 = dangerous to all humans
inversion

## Slide 11: Primary pollutants
Sulfur dioxide
Nitrogen dioxide
Carbon monoxide
Volatile organic compounds (VOCs)
Hazardous air pollutants (HAPs)(e.g. lead, etc)
Notes: VOCs – released from burning fuel. Some examples: formaldehyde, benzene, toluene, styrene, xylene, perchloroethylene.

## Slide 12: Secondary pollutants
Pollutants that are formed from chemical or photochemical reactions of primary pollutants
  Ozone (VOCs + NOx -> ozone)
  Nitric acid (HNO3)
  Formaldehyde
  Particulate nitrate (acid rain)
  Particulate sulfate (acid rain)

## Slide 13
Greenberg MI, ed. Occupational, industrial, and environmental toxicology, 2nd edition. Mosby, 2003

## Slide 14: Individual agents
Sulfur dioxide (SO2)
Oxides of nitrogen (e.g. nitrogen dioxide, NO2)
  Acid rain
Ozone (O3)
Carbon monoxide (CO)
Particulate matter (PMs)
Lead, metals, and other hazardous air pollutants (HAPs) or “air toxics”

## Slide 15: Sulfur dioxide
Primary source = coal power plants
Sulfur dioxide(SO2) -> sulfuric acid (H2SO4)
  In atmosphere and in respiratory tract
Water soluble irritant gas
  Upper airway deposition
  Produces sulfurous acid, bisulfite, sulfite, and H2SO4
    Bronchoconstriction (bisulfite)
    Upper airway irritation
    Inflammatory/immune responses - sensitizer

## Slide 16: Nitrogen dioxide
Primary source is automobiles, then power generation, biomass burning(local)
N2 and O2 combine to form Nox
NO2 combines with water in lungs to form nitrous acid and nitric acid
  Bronchospasm/airway hyperresponsiveness
  Increased susceptibility to airway infections (chronic)

## Slide 17: Sulfur dioxide and nitrogen dioxide
Non-medical, environmental effects

## Slide 18: Acid Rain

## Slide 19: Acid rain

## Slide 20: Acid rain

## Slide 21: Ozone
Stratospheric (“good”) ozone
Ground-level (“bad”) ozone
  Created by reaction of NOx and VOCs and sunlight
    NOx released from energy production
    VOCs released from energy production, automobiles, and natural sources
      Ozone generally highest in afternoon w/ sunny weather (summer)
Remains the most violated environmental standard in the United States
Main component of smog

## Slide 22: Ozone
Health effects:
  Low water solubility – alveoli
  Irritant and oxidant -> pulmonary inflammation
    Bronchospasm (cough, wheeze, chest tightness)
    Decreased FVC and FEV1
  Short term:
    Increases in admissions for pneumonia, COPD, asthma, respiratory complaints
      Reversible (decreased asthma complaints in Atlanta, US after reduced traffic/ozone during Olympic games)
    Increased mortality rates on days with high ozone from cardiopulmonary disorders
  Long-term -> increased chronic respiratory illnesses (in lab animals)

## Slide 23: Carbon monoxide
Primary source = automobiles
Systemic effects:
  Decreases oxygen delivery
Acute toxicity
Chronic toxicity:
  Increased events in patients with chronic cardiopulmonary diseases: angina, MI.

## Slide 24: Particulate matter (PMs)
Solid and liquid components of airborne aerosol
  Acid sulfate and nitrates formed from SO2 and NOx
  Ammonium nitrate and sulfates
  Particulates from diesel exhaust, wood burning, dust, road surfaces, and elemental carbon

## Slide 25: Particulate matter (PMs)
Large particles > 10 µm
  Deposit in upper airways
Coarse particles = 2.5-10 µm (PM10)
  Airborne dust, crustal elements (silicon, aluminum)
  Deposit in lower airways
Fine particles < 2.5 µm (PM2.5)
  Acid sulfates and nitrates
  Deposit in alveoli & have systemic effects
Total suspended particulates (TSP)

## Slide 26: Particulate matter (PMs)
Health effects:
  PM10 associated with:
    Increases in asthma and COPD exacerbations

## Slide 27: Particulate matter (PMs)
Health effects:
  PM2.5 associated with:
    Increased mortality
    PM2.5 concentration correlates with
      Increased histamine release in airways
      Reduced macrophage activity in lungs (decreased response to infection?)
      Decreased heart rate variability (marker for MI risk)
      Increased ICD discharges
      Increased plasma viscosity

## Slide 28: Particulate matter (PMs)
Harvard Six Cities Study
For each 10µg/m3 increase in PM2.5:
  1.5% daily increase in mortality
  3.3% daily increase in COPD deaths
  2.1% daily increase in ischemic heart disease deaths

## Slide 29: Hazardous air pollutants (HAPs)
US EPA introduced HAPs in 1997
189 chemicals
  VOCs
  Metals
  Important chemicals: benzene, arsenic, lead, mercury

## Slide 30: Hazardous air pollutants (HAPs)
33 HAPs that are “most hazardous to human health”

## Slide 31: Patterns of air pollution
Natural peaks and valleys
  SO2, CO – cold weather
  NO2 - mid-day
  O3 - mid-day, sunny weather (summer)

## Slide 32: Air Quality Index
0-500
100 = PEL
AQI = the highest AQI number for any of the pollutants
Non-linear

## Slide 33: Air Quality Index
0-500

## Slide 34: US Regulation
1955, Air Pollution Control Act
1965 Motor Vehicle Air Pollution Control Act
1963 Clean Air Act
  Amended 1970, 1977, 1990

## Slide 35: Clean Air Act
Established National Ambient Air Quality Standards (NAAQS) to protect public health
  Primary standards – to protect public health
  Secondary standards – to protect welfare (against decreased visibility and damage to crops, buildings, etc)
  US EPA responsible for establishing and revising
    If a county is designated as a nonattainment area, then the state is mandated to develop a plan to bring the county into attainment
    States also issue permits for large stationary sources of criteria pollutants

## Slide 36: US National Ambient Air Quality Standards

## Slide 37: Clean Air Act
Determined “criteria pollutants”:
  NO2, SO2, CO, O3, Lead, PM2.5, PM10
1990 Clear Air Act amendment
  189 additional pollutants (“hazardous air pollutants”, HAPs)
    33 posing the greatest threat to public health
    Phase 1:
      Maximum achievable control technology (MACT)
      Determined by EPA
      Required for all sources of HAPs

## Slide 38: Monitoring

## Slide 39: Has regulation worked?

## Slide 40
Nitrogen dioxide
PM2.5

## Slide 41
Lead
Ozone

## Slide 42: Effective controls for outdoor air pollution
Control of SO2 requires regulation of coal-fired energy production
  Reduced sulfur coal (and gas and diesel)
  Engineering controls at energy production facilities
Notes: Thai automobile emissions standards 1995

## Slide 43: Effective controls for outdoor air pollution
Regulation of automobile pollution:
Fuel reformulation:
  Leaded gas discontinued
  Decrease benzene content to <3.5%
  Increased oxygen content (MTBE, ethanol)
  Diesel and gasoline sulfur reduction
Automobile emission standards
Notes: Thai automobile emissions standards 1995
Leaded gas discontinued in 1996

## Slide 44: Effective controls for outdoor air pollution
Catalytic converters (1975,1993)
  Catalyze redox reactions
    Combine CO w/ O2 to form CO2
    Oxidize unburned hydrocarbons to form CO2 and H2O
    “Three-way” CC also reduce NOx to N2 and O2

## Slide 45: Effective controls for outdoor air pollution
Regulation of fixed site polluters (HAPs)
  Require fixed site polluters to use engineering controls
    Catalytic converters for smoke stacks
    Updating processes
    Finding alternative raw materials or catalysts

## Slide 46: Local resources
Monitoring stations
Air Quality – real time reporting

## Slide 47: Monitoring

## Slide 48: Aqicn.org/city/bangkok/

## Slide 49: Thai Air Quality Standards
Pollutant | Time Period | Concentration
SO2 | Annual | .10 mg/m3 (0.04 ppm)
 | 24 hours | .30 mg/m3 (0.12 ppm)
 | 1 hour | 780 mcg/m3 (0.3 ppm)
NO2 | 1 hour | 0.32 mg/m3 (0.17 ppm)
 | Annual | 0.057 mg/m3 (0.03 ppm)
PM10 | Annual | 0.05mg/m3
 | 24 hours | 0.12 mg/m3
PM2.5 | Annual | 0.025 mg/m3
 | 24 hours | 0.05 mg/m3
O3 | 8 hours | 0.14 mg/m3 (0.07 ppm)
 | 1 hour | 0.20 mg/m3 (0.10 ppm)
Lead (Pb) | Monthly | 1.5 mcg/m3
CO | 8 hours | 10.26 mg/m3 (9 ppm)
 | 1 hour | 34.2 mg/m3 (30 ppm)

## Slide 50: Conclusions
Air pollution:
  Is a complicated mixture of primary pollutant as well as secondary pollutants
  May lead to increases in respiratory complaints/infections as well as increased mortality from respiratory and cardiovascular illnesses
  May be controlled by strict regulation of source polluters and vehicles
  Is monitored in real-time in many locations

## Slide 51: QUESTIONS?