## Slide 1: Petrochemical industry
Rob Hendrickson, MD

## Slide 2: Objectives
Process
Clinical effects
  Acute/subacute toxicity
  Chronic toxicity
Mitigation, monitoring, and safety

## Slide 3: Petroleum refining

## Slide 4: Petroleum refining
Conversion of crude oil to usable products
Crude oil = ‘crude petroleum’
  Organic matter
    Converted via bacteria & low temp chemical reactions to kerogen (complex solid w HMW molecules)
    Converted to bitumen (complex HWM hydrocarbons; e.g. tars)
    Converted to liquid petroleum (HMW hydrocarbons [C15-40] with high sulfur content)
    Under higher pressure and temperature, converted to LMW hydrocarbons (C<15) with less sulfur

## Slide 5
Notes: Gulf of Thailand

## Slide 6: Crude Oil
Crude oil
  Significant variability of content throughout the world
    84-87% carbon
    11-14% hydrogen
    0-3% sulfur
    0.2% nitrogen
    0.2-7% Polycyclic aromatic hydrocarbons
    0.01-1% Benzene

## Slide 7: Crude Oil
Crude oil
  Combination of many hydrocarbons (C1-50)
    Aliphatic/paraffin compounds
      saturated hydrocarbons
    Naphthene compounds
      Saturated cyclic hydrocarbons
    Aromatic compounds
      Cyclic hydrocarbons with alternating single and double bonds
Notes: Aliphatic – saturated hydrocarbon (no double bonds). May be straight or cyclic.
Naphthene – saturated and cyclic. Cyclohexane is the example above.
Aromatic – cyclic with alternating double and single bonds.

## Slide 8: Crude Oil
Crude oil
  ‘Sweet crude’ – low sulfur
    < 5 ppm hydrogen sulfide
  ‘Sour crude’ – high sulfur
    > 5 ppm hydrogen sulfide (sometimes up to 100,000 ppm)
  Paraffinic base – large [] of straight hydrocarbons
  Naphthenic base – large [] of saturated rings with side chains
  Aromatic base – large [] of aromatics

## Slide 9: Petroleum refining
Separation of hydrocarbons – by carbon length
  Distillation
  Cracking
  Reforming

## Slide 10
Fractionated distillation

## Slide 11: Vacuum distillation
Additional distillation to separate the heavier hydrocarbons
  Heavier hydrocarbons have higher boiling points
  These high temperatures would cause degradation of molecules (“cracking”), so distillation is performed in a vacuum to lower boiling temperature
Distillation
Notes: Water boils at 88C at 11,000 feet.

## Slide 12
Distillation

## Slide 13: Cracking
Heat and catalysts to break down (“crack”) large molecules into smaller molecules
  Thermal cracking (high pressure)
  Catalytic cracking (“cat cracking”)
    Zeolite = aluminum & silicon
  Steam cracking (brief, high temp, no oxygen)
  Hydrocracking (hydrogen)
Generally used to produce gasoline (petrol), with carbon chains of 5-10
Distillation

## Slide 14: Reforming
Converting straight hydrocarbons to branched hydrocarbons or aromatics (can be used for increasing octane in gasoline)
  Platinum catalyst

## Slide 15: Coking
Catalytic and thermal separation of heavy residue oil
Results in separation of lighter oils and leaves “coke”
  Coke = 95% carbon
    Used for:
      heating (smokeless burning)
      Production of electrodes
        aluminum and steel industries

## Slide 16
Petrochemicals

## Slide 17: Clinical toxicities

## Slide 18: Acute/subacute
Acute event of greatest concern = explosion and fire

## Slide 19: Acute/subacute
Acute toxicities
  CNS effects:
    Hydrocarbons
    Carbon monoxide (CO)
    Hydrogen Sulfide (H2S)
  Mucosal and dermal irritation

## Slide 20: CNS depressants
Closed systems
Detectors
PPE

## Slide 21: Hydrocarbons
Short carbon chain hydrocarbons
  Inhalational route
  Carbon chains 3-10 in length
    E.G. propane, butane, pentane, hexane, etc
  CNS depression
  Simple asphyxiants
Result of releases, leaks, fugitive emissions
  low [] of hydrocarbon in refinery air

## Slide 22: Hydrocarbons
Treatment:
  Removal from exposure
Mitigation:
  Avoid exposure!
    Enclosed space processes
    Monitoring
    Enclosed systems

## Slide 23: Carbon monoxide
Colorless, odorless – poor warning properties
Symptoms:
  Mild: Headache, nausea/vomiting, confusion
  Severe: Cardiac & Neurologic toxicity
Mechanism
  Binds to hemoglobin & myoglobin
  Inhibits oxidative phosphorylation
  Displaces NO
Notes: CO causes hemoglobin to hold O2 closer and not deliver O2 to the tissues. (left shift of the oxy-hgb dissociation curve)

## Slide 24: Carbon monoxide
Treatment:
  Removal from exposure
  Oxygen
  Hyperbaric oxygen
Mitigation:
  Engineering controls
  Detectors

## Slide 25: Hydrogen Sulfide
Moderately water soluble irritant gas
  Mild, delayed mucosal irritation
Systemic effects
  Inhibiting oxidative phosphorylation
    “cyanide-like” effects – inhibition of cytochrome aa3
    “knock down”
    Multi-organ failure
    Multiple casualties

## Slide 26: Hydrogen Sulfide
Poor warning properties
  Potent smell of rotten eggs
  Olfactory fatigue – smell less at stable []
  Olfactory paralysis – less odor at higher []

## Slide 27: Hydrogen Sulfide
Concentration dependent effects:
  0.02ppm “rotten egg” odor
  50ppm MM irritation, N/V/D
  100ppm sweet smell
  150ppm no odor. + ataxia, lightheadedness, ALI
  500ppm loss of consciousness (seconds)
    Respiratory paralysis, asphyxia

## Slide 28: Hydrogen Sulfide
Exposure due to:
  spill/release
  Enclosed space

## Slide 29: Hydrogen Sulfide
Treatment
  Oxygen
  ??? Nitrites – probably not effective
  ? HBO – elevates dissolved oxygen
    May increase diffusion of oxygen to marginally perfused tissue
    May decrease H2S binding to cytochrome oxidase
Notes:   Nitrites: – produce methemoglobin which binds to H2S to form sulfmethemoglobin which is metabolized by rhodanase

## Slide 30: Subacute
Dermatitis/irritant/skin sensitizers
  MTBE (additive in gasoline)
  H2S
  Cutting oils
  Aminated alkylaryl polyether compounds
  Alkylaryl sulfonate compounds
  Ethylene diamine
  Alkylamines

## Slide 31: Chronic
Cancer risk
  Epidemiologic studies
    Mixed
    Suggest that there is no increased risk of cancer in petroleum refinery workers
  Handling known human carcinogens
    Benzene
    PAHs, benzo[a]pyrene

## Slide 32: Benzene
Contained in crude oil and finished products (e.g. gasoline)
  IARC 1 known human carcinogen
    Acute myelogenous leukemia
  Found in very low quantities in vapor

## Slide 33: PAHs
Polycyclic aromatic hydrocarbons
  Organic compounds with >=3 aromatic rings
    Most carcinogenic PAHs have 5 or 6 rings
Notes: Benzo[a]pyrene, dibenz[a,c]anthracene, chrysene, 1-nitropyrene

## Slide 34: PAHs
Polycyclic aromatic hydrocarbons
  Found in crude oil and in middle and heavy distillate fraction
    Exposures: cracking, coking, and asphalt processing
      Mostly to lighter, 2-3 aromatic ring PAHs that have little to no carcinogenicity
  Inhalation or dermal absorption
Notes: Benzo[a]pyrene, dibenz[a,c]anthracene, chrysene, 1-nitropyrene

## Slide 35: PAHs
Benzo[a]pyrene
  IARC 1 carcinogen
  Primary carcinogen responsible for:
    Lung cancer from cigarette smoke
    Scrotal cancer in chimney sweeps (1800s)
  Procarcinogen – CYP1A1
    benzo[a]pyrene-7,8-dihydrodiol-9,10-epoxide
Notes: Benzo[a]pyrene, dibenz[a,c]anthracene, chrysene, 1-nitropyrene
BaP is metabolized by CYP1A1 to epoxide via a 3 step process. The “ultimate carcinogen” = bap-7,8-dihydrodiol-9,10-epoxide

## Slide 36: Protection of workers
Engineering controls
  Closed systems
Airborne monitoring
  CO, H2S
Periodic exam and questionnaire
  Inhaled irritants
  Dermal sensitizers
Notes: Biomonitoring – total urine (end of shift) phenols for benzene;

## Slide 37: Questions and discussion…