## Slide 1: Ship- and boat-building industries
Rob Hendrickson, MD

## Slide 2: Objectives
Industry
Process, jobs, and toxicity associated with:
  Shipbuilding
  Boatbuilding
  Ship breaking

## Slide 3: Ship vs. Boat
Notes: Purposes of this discussion:
ship = metal hull
boat = fiberglass hull

## Slide 4: Industry
U.S.
  First Tier (6), (ships > 383 feet)
  569 total shipyards
  111,905 employees
US$25 billion
Spring 2015 Industry Study; Shipbuilding, Dwight D. Eisenhower School for National Security and Resource Strategy; National Defense University;
http://es.ndu.edu/Portals/75/Documents/industry-study/reports/2015/es-is-report-shipbuilding-2015.pdf

## Slide 5: Industry
Shipbuilding and repairing industry in Thailand; Thai Shipbuilding and repairing industry; www.asef2015.com/asef2007/PDF/3.%20Shipbuilding_Industry_in_Thailand.pdf

## Slide 6
Shipbuilding and repairing industry in Thailand; Thai Shipbuilding and repairing industry; www.asef2015.com/asef2007/PDF/3.%20Shipbuilding_Industry_in_Thailand.pdf

## Slide 7: Shipbuilding - Thailand
Offshore support vessels
Naval vessels
Merchant vessels
Notes: 250 offshore platforms operating in the Gulf of Thailand

## Slide 8: Process
Huge industry with many varied skilled laborers
Hull block construction method

## Slide 9: Process

## Slide 10: Process

## Slide 11: Process

## Slide 12: Process

## Slide 13: Process

## Slide 14: Process

## Slide 15: Process

## Slide 16: Process
Some example jobs:
  Small parts production / paint removal
  Welders
  Machining
  Painters
  Electricians
  Pipefitters
  Laggers

## Slide 17: Process
Paint removal/Steel prep
  Solvents / degreasers
  Pickling(rust protection) – dip tanks of heated caustic soda, alkali rinse (pH 8-13), heated sulfuric acid, phosphoric acid
  Blasting
    Metal filings, copper slag, steel grit or shot, or sand (silica).
Notes: Blasting – Sand, metal filings, copper slag, steel grit or shot.
Solvents – acute inebriation, lightheadedness; chronic neurologic

## Slide 18: Simple Silicosis
Crystalline silica 0.5-3 micrometers
Ingested by macrophages
  -> inflammatory mediators
CXR nodular opacities
Pulmonary testing:
  Restrictive pattern
    Decreased FEV1, FVC, TLC
Notes: Blasting – Sand, metal filings, copper slag, steel grit or shot.

## Slide 19: Simple Silicosis
Notes: Annual CXR, PFTs, and medical examination

## Slide 20: Silicosis
Chronic simple silicosis
  >10 years; <1cm nodules
Accelerated silicosis
  5-10 years; progress rapidly
Complicated silicosis
  Progressive massive fibrosis; >1cm nodules
Acute
  Weeks-5years; ground-glass; alveolar silica
Notes: Blasting – Sand, metal filings, copper slag, steel grit or shot.

## Slide 21: Process
Laggers
  Apply asbestos / MMFs to pipes and surfaces
Notes: Welding – joining 2 pieces of metal

## Slide 22: Asbestos
Replaced by MMFs in 1975 in US
Asbestosis – diffuse interstitial fibrosis
  Dose response
  Latency of 20-40 years
  More frequent in smokers
  “frustrated macrophage” theory
  PFTs – restrictive lung disease, decreased diffusion
  Cancer – lung cancer, mesothelioma
Notes: Monitoring – annual exam, CXR, PFTs, PPD

## Slide 23: MMMFs
Man made mineral fibers
  Skin/respiratory irritant
  Chronic bronchitis
  Elevated risk of small CXR opacities
  No clear risk with cancer
Notes: Welding – joining 2 pieces of metal

## Slide 24: Process
Welders
  Enclosed spaces, poor ventilation
  CO, ozone, NO2
  Metals (iron, lead, arsenic, manganese, zinc, nickel, chromium, cobalt, copper)
    Leaded paint (military vessels)
  Chemicals released from metal surface: solvents, phosgene, fluoropolymers, degreasers, fuels
Notes: Welding – joining 2 pieces of metal

## Slide 25: Process
Machining
  Drilling, grinding, and milling
  Cutting fluids/oils, lubricants, greases, solvents
Notes: Welding – joining 2 pieces of metal

## Slide 26: Process
Painters
  Leaded and unleaded paint
  Exposure to asbestos/MMF, paint thinners, resins
  Marine paint
    Anti-fouling paints
      Copper paint – hemolysis, hepatotoxicity, renal toxicity
      Organotin / tributyltin oxide – MM irritation,
      “Hard bottom paints”
        Teflon – polymer fume fever
Notes: Welding – joining 2 pieces of metal

## Slide 27: Process
Electricians
  Enclosed spaces
  Exposed to welding fumes, asbestos/MMFs, when in proximity to welders, pipefitters, etc
Notes: Welding – joining 2 pieces of metal

## Slide 28: Process
Pipefitters
  Welding, boring
  Asbestos/MMFs
Notes: Welding – joining 2 pieces of metal

## Slide 29: Boatbuilding
Notes: Welding – joining 2 pieces of metal

## Slide 30: Boatbuilding
Mold – wood/plastic
Covered by brush or spray with resin/fiberglass
  Resins- polyesters, epoxies, polyamides, phenolics
  Solvents – styrene, methylethylketone(MEK), acetone, methanol
  Catalysts
  Pigments
Notes: Welding – joining 2 pieces of metal

## Slide 31: Boatbuilding
Notes: Fiberglass or glass-reinforced plastic

## Slide 32: Styrene
Vinyl benzene (C8H8) – slightly yellow, oily liquid, pungent sweet odor
Acute exposure = mucosal irritation(115ppm), inebriation and ataxia (375ppm)
Chronic exposure = M/S neuropathy, neurobehavioral effects
Metabolized to styrene 7,8-oxide, decreases brain glutathione and leads to oxidative damage
Further metabolized to mendelic acid and phenyl glyoxylic acid
Notes: Fiberglass or glass-reinforced plastic

## Slide 33: Methyl ethyl ketone
MEK, 2-butanone
Acute exposure – mucosal irritation, inebriation, headache
Little evidence of chronic neurotoxicity – studies include patients exposed to multiple solvents.
Notes: Fiberglass or glass-reinforced plastic

## Slide 34: Shipbreaking
Notes: Bangladesh

## Slide 35: Shipbreaking
Notes: India

## Slide 36: Shipbreaking
Notes: Fiberglass or glass-reinforced plastic

## Slide 37: Shipbreaking
Notes: Fiberglass or glass-reinforced plastic

## Slide 38: Shipbreaking
Notes: Bangladesh

## Slide 39: Ship building
Increasingly large business in the US and Thailand
  Enclosed spaces
  Silica, metals, solvents
  Copper
  Asbestos, MMFs
Notes: Bangladesh

## Slide 40: Boat building
Increasingly large business in the US and Thailand
  Enclosed spaces
  Solvents
  Styrene
  MEK
Notes: Bangladesh

## Slide 41: Ship breaking
Large business in India, Bangladesh, China
Occupational physical hazards
Toxicological hazards:
  Metals, asbestos, MMFs
  Paints, solvents
Notes: Bangladesh

## Slide 42: Questions and discussion…