## Slide 1: Outdoor air pollution
Robert G. Hendrickson, MD
Oregon Poison Center
Oregon Health and Science University
Portland, Oregon, USA

## Slide 2: Outdoor air pollution
What is outdoor air pollution?
  Gases & fine particles produced from natural and man-made activities
  Smog = used to describe mixture of smoke/pollution and fog

## Slide 3: Bangkok

## Slide 4: Beijing

## Slide 5: New York City

## Slide 6: Salt Lake City, UT

## Slide 7: Los Angeles

## Slide 8: Outdoor air pollution
What is outdoor air pollution?
  Oxides of nitrogen (e.g. nitrogen dioxide, NO2)
  Sulfur dioxide (SO2)
  Ozone (O3)
  Carbon monoxide (CO)
  Particulate matter (PMs)
  Lead, metals, and other hazardous air pollutants (HAPs) or “air toxics”

## Slide 9: Primary pollutants
Sulfur dioxide
Nitrogen dioxide
Carbon monoxide
Volatile organic compounds (VOCs)
Hazardous air pollutants (HAPs)(e.g. lead, etc)
Notes: VOCs – released from burning fuel. Some examples: formaldehyde, benzene, toluene, styrene, xylene, perchloroethylene.

## Slide 10: Secondary pollutants
Pollutants that are formed from chemical or photochemical reactions of primary pollutants
  Ozone (VOCs + NOx -> ozone)
  Nitric acid (HNO3)
  Formaldehyde
  Particulate nitrate (acid rain)
  Particulate sulfate (acid rain)

## Slide 11
Greenberg MI, ed. Occupational, industrial, and environmental toxicology, 2nd edition. Mosby, 2003

## Slide 12: Individual agents
Sulfur dioxide (SO2)
Oxides of nitrogen (e.g. nitrogen dioxide, NO2)
  Acid rain
Ozone (O3)
Carbon monoxide (CO)
Particulate matter (PMs)
Lead, metals, and other hazardous air pollutants (HAPs) or “air toxics”

## Slide 13: Sulfur dioxide
Primary source = coal power plants
Sulfur dioxide(SO2) -> sulfuric acid (H2SO4)
  In atmosphere and in respiratory tract

## Slide 14: Sulfur dioxide
Water soluble irritant gas
  Upper airway deposition
  Produces sulfurous acid, bisulfite, sulfite, and H2SO4
    Bronchoconstriction (bisulfite)
    Upper airway irritation
    Inflammatory/immune responses - sensitizer

## Slide 15: Nitrogen dioxide
Primary source is automobiles, then power generation, biomass burning(local)
N2 and O2 combine to form NOx
NO2(and PM) – give smog its red/brown color

## Slide 16: Nitrogen dioxide
NO2 combines with water in lungs to form nitrous acid and nitric acid
  Bronchospasm/airway hyperresponsiveness
  Increased susceptibility to airway infections (chronic)

## Slide 17: Ozone
Stratospheric (“good”) ozone
Ground-level (“bad”) ozone
  Created by reaction of NOx and VOCs and sunlight
    NOx released from energy production
    VOCs released from energy production, automobiles, and natural sources
      Ozone generally highest in afternoon w/ sunny weather (summer)

## Slide 18: Ozone
Ground-level (“bad”) ozone
  Remains the most violated environmental standard in the United States
  Main component of smog

## Slide 19: Ozone
Health effects:
  Low water solubility – alveoli
  Irritant and oxidant -> pulmonary inflammation
    Bronchospasm (cough, wheeze, chest tightness)
    Decreased FVC and FEV1

## Slide 20: Ozone
Health effects:
  Short term:
    Increases in admissions for pneumonia, COPD, asthma, respiratory complaints
      Reversible (decreased asthma complaints in Atlanta, US after reduced traffic/ozone during Olympic games)
    Increased mortality rates on days with high ozone from cardiopulmonary disorders
  Long-term:
    Increased chronic respiratory illnesses (in lab animals)

## Slide 21: Carbon monoxide
Primary source = automobiles
Systemic effects:
  Decreases oxygen delivery
Acute toxicity
Chronic toxicity:
  Increased events in patients with chronic cardiopulmonary diseases: angina, MI.

## Slide 22: Particulate matter (PMs)
Solid and liquid components of airborne aerosol
  Acid sulfate and nitrates formed from SO2 and NOx
  Ammonium nitrate and sulfates
  Particulates from diesel exhaust, wood burning, dust, road surfaces, and elemental carbon

## Slide 23: Particulate matter (PMs)
Large particles > 10 µm
  Deposit in upper airways
Coarse particles = 2.5-10 µm (PM10)
  Airborne dust, crustal elements (silicon, aluminum)
  Deposit in lower airways
Fine particles < 2.5 µm (PM2.5)
  Acid sulfates and nitrates
  Deposit in alveoli & have systemic effects
Total suspended particulates (TSP)

## Slide 24: Particulate matter (PMs)
Health effects:
  PM10 associated with:
    Increases in asthma and COPD exacerbations

## Slide 25: Particulate matter (PMs)
Health effects:
  PM2.5 associated with:
    Increased mortality
    PM2.5 concentration correlates with
      Increased histamine release in airways
      Reduced macrophage activity in lungs (decreased response to infection?)
      Decreased heart rate variability (marker for MI risk)
      Increased ICD discharges
      Increased plasma viscosity

## Slide 26: Particulate matter (PMs)
Harvard Six Cities Study
For each 10µg/m3 increase in PM2.5:
  1.5% daily increase in mortality
  3.3% daily increase in COPD deaths
  2.1% daily increase in ischemic heart disease deaths

## Slide 27: Hazardous air pollutants (HAPs)
US EPA introduced HAPs in 1997
189 chemicals
  VOCs
  Metals
  Important chemicals: benzene, arsenic, lead, mercury

## Slide 28: Hazardous air pollutants (HAPs)
33 HAPs that are “most hazardous to human health”

## Slide 29: Patterns of air pollution
Natural peaks and valleys
  SO2, CO – cold weather
  NO2 - mid-day
  O3 - mid-day, sunny weather (summer)
Notes: SO2 = coal powered plants – more when it is cold
NO2 = automobiles – more while cars are on the road

## Slide 30: Air Quality Index
0-500
100 = PEL
AQI = the highest AQI number for any of the pollutants
Non-linear

## Slide 31: Air Quality Index
0-500
Notes: 53 = air quality is acceptable, but a small # of people may have increased pulmonary complaints

## Slide 32: US Regulation
1955, Air Pollution Control Act
1965 Motor Vehicle Air Pollution Control Act
1963 Clean Air Act
  Amended 1970, 1977, 1990

## Slide 33: Clean Air Act
Established National Ambient Air Quality Standards (NAAQS) to protect public health
  US EPA responsible for establishing and revising
    If a county is designated as a nonattainment area, then the state is mandated to develop a plan to bring the county into attainment
    States also issue permits for large stationary sources of criteria pollutants

## Slide 34: National Ambient Air Quality Standards
Pollutant | Time | Thai NAAQS | US NAAQS | WHO
PM2.5 | 24h 1year | - - | 35 mcg/m3 15 mcg/m3 | 25 mcg/m3 10 mcg/m3
PM10 | 24 h 1 year | 120 mcg/m3 50 mcg/m3 | 150 mcg/m3 | 50 mcg/m3 20 mcg/m3
Pb | 1 month 1 year | 1.5 mcg/m3 | 0.15 mcg/m3 (quarterly) | 0.5 mcg/m3
SO2 | 1 hour 24 hour 1 year | 780 mcg/m3 300 mcg/m3 100 mcg/m3 | 197 mcg/m3 | 20 mcg/m3
NO2 | 1 hour 1 year | 320 mcg/m3 | 188 mcg/m3 100 mcg/m3 | 200 mcg/m3 40 mcg/m3
Ozone | 1 hour 8 hours | 200 mcg/m3 140 mcg/m3 | 140 mcg/m3 | 100 mcg/m3
CO | 1 hour 8 hours | 34.2 ppm 10.3 ppm | 35 ppm 9 ppm | 30 ppm 10 ppm

## Slide 35: Clean Air Act
Determined “criteria pollutants”:
  NO2, SO2, CO, O3, Lead, PM2.5, PM10
1990 Clear Air Act amendment
  189 additional pollutants (“hazardous air pollutants”, HAPs)
    33 posing the greatest threat to public health
    Phase 1:
      Maximum achievable control technology (MACT)
      Determined by EPA
      Required for all sources of HAPs

## Slide 36: Aqicn.org
http://www.deq.state.or.us/aqi/index.aspx

## Slide 37: Bangkok, Thailand

## Slide 38: Conclusions
Air pollution:
  Is a complicated mixture of primary pollutant as well as secondary pollutants
  May lead to increases in respiratory complaints/infections as well as increased mortality from respiratory and cardiovascular illnesses
  May be controlled by strict regulation of source polluters and vehicles
  Is monitored in real-time in many locations

## Slide 39: Questions?

## Slide 40: Has regulation worked?

## Slide 41
Nitrogen dioxide
PM2.5

## Slide 42: Effective controls for outdoor air pollution
Regulation of coal-fired energy production and fixed site polluters (HAPs)
  Reduced sulfur coal (and gas and diesel)
  Engineering controls at energy production facilities
    Catalytic converters for smoke stacks
    Finding alternative raw materials or catalysts
Notes: Thai automobile emissions standards 1995

## Slide 43: Effective controls for outdoor air pollution
Regulation of automobile pollution:
  Fuel reformulation:
    Leaded gas discontinued (1996, Thailand)
    Decrease benzene content to <3.5%
    Increased oxygen content (MTBE, ethanol)
    Diesel and gasoline sulfur reduction
  Automobile emission standards (1995, Thailand)
Notes: Thai automobile emissions standards 1995
Leaded gas discontinued in 1996

## Slide 44: Effective controls for outdoor air pollution
Catalytic converters (1975)
  Catalyze redox reactions
    Combine CO w/ O2 to form CO2
    Oxidize unburned hydrocarbons to form CO2 and H2O
    “Three-way” CC also reduce NOx to N2 and O2

## Slide 45: Sulfur dioxide and nitrogen dioxide
Non-medical, environmental effects

## Slide 46: Acid Rain
Sulfuric acid
Nitric acid
Notes: Sulfuric acid and nitric acid
pH can be as low as 5 in NE US.

## Slide 47: Acid rain

## Slide 48: Acid rain

## Slide 49: Acid rain